## Slide 1
TECHNICAL APPROACH
DRISHTI — District Risk Intelligence and Satellite Hazard Tracking Interface · SIH26191
System Architecture & Workflow
FRONTEND — vanilla JS + Leaflet, no build step
• Live board, click-to-justify red zones, district & national views
• One state object drives every screen; no framework, no bundler
BACKEND — FastAPI + NumPy physics engine
• Terrain hydrology: D8 flow routing, HAND, slope, wetness index
• Hazard models: BIS IS 14496 (landslide), SCS-CN→Manning (flood), IMD threshold (cloudburst), Bruun (erosion)
DATA LAYER — zero API keys, anywhere
• Baked real: Copernicus DEM · GHS-POP · GHSL · WorldCover · OpenStreetMap · geoBoundaries · IBTrACS
• Live feeds: Open-Meteo — rainfall, CAPE, soil moisture, cloud structure
DATA FLOW
Terrain + satellite data → per-cell hazard physics → Red Zone recurrence index → relocation site allocation + live monitoring
LIVE / RESPONSE LOOP
Live weather → cloud-pattern read (no ML) → urgency ranking → force-refresh proof → district drill-down → click-to-justify
PROCESS FLOW ARCHITECTURE
BAKED REAL DATA
DEM · Population · Built-up · Roads
LIVE FEEDS (Open-Meteo)
Rainfall · CAPE · Soil · Cloud
TERRAIN ENGINE — core/terrain.py
D8 flow routing · HAND · slope · topographic wetness index
HAZARD PHYSICS — five modules, one recurrence scale
Flood · Landslide (BIS LHEF) · Cloudburst (IMD) · Erosion · Waterlogging
RED ZONE ENGINE — core/redzone.py
Shortest return period (5 / 25 / 100-yr) at which a cell turns uninhabitable
RELOCATION ENGINE
Siting + capacity math
LIVE WATCH BOARD
Urgency ranking, live
CLICK-TO-JUSTIFY
Per-cell explain API
FRONTEND — Leaflet map + panels
→ District Magistrate / SDMA decision