## Slide 1
SMART INDIA HACKATHON 2026
DRISHTI
District Risk Intelligence & Satellite Hazard Tracking Interface
We keep rebuilding villages
in the same death trap.
A GIS decision-support platform that identifies multi-hazard Red Zones unsuitable for permanent habitation, assesses the carrying capacity of safer sites, and ranks vulnerable habitations for relocation.
PROBLEM STATEMENT ID
SIH26191
PROBLEM STATEMENT TITLE
Hazard-Based Red Zones, Carrying Capacity & Relocation Needs
ORGANISATION
Ministry of Home Affairs
DEPARTMENT
NDRF, DM Division
THEME
Disaster Management
PS CATEGORY
Software
TEAM ID / NAME
<< enter Team ID and Name >>
Notes: Fill in the team ID and name before submitting. Everything else is fixed by the problem statement.

## Slide 2
IDEA AND APPROACH DETAILS
Proposed Solution
Not where the water is today — whether anyone should be living there at all.
HOW IT WORKS
DRISHTI runs the hazard model at the 5-, 25- and 100-year event and records, for every 160 m cell, the shortest return period at which any of four hazards renders it uninhabitable. That single number — years between events that make a place unliveable — is the Red Zone index. It is physically meaningful, and it maps directly onto a relocation horizon: immediate, short-term or medium-term.
HOW IT ADDRESSES THE PROBLEM
Current relocation is reactive — it starts after a disaster, when the evidence is a body count. Severity of one event tells you almost nothing: a place flooded chest-deep once a century is a place you protect; the same depth every fifth monsoon is a place you move. Recurrence is what separates the two, and it is what no existing portal reports.
INNOVATION AND UNIQUENESS
Recurrence, not severity
The return period at which land becomes uninhabitable — the number a relocation decision actually needs.
The Indian standard, implemented
Landslide hazard follows BIS IS 14496 (Part 2), the LHEF scheme GSI uses — not an invented overlay.
Four hazards, one index
Flood, landslide, waterlogging and coastal erosion combined by dominance, with the governing hazard named.
Capacity, not just safety
Sites are scored on safety, buildability and room — and the allocator respects capacity rather than assuming it.
Distance is a cost, not a footnote
Resettlement fails when people are moved from their fields. Mean displacement is minimised and reported.

## Slide 3
TECHNICAL APPROACH
Technologies and Methodology
Every step is a published method. Physics first, because a relocation order has to survive an inquiry.
PROCESS FLOW
TERRAIN
DEM to HAND, slope, wetness, D8 drainage
HAZARD
Flood · landslide waterlogging · erosion, x3 events
RECURRENCE
Return period at which land turns uninhabitable
EXPOSE
Dasymetric population, roads, facilities
RELOCATE
Site capacity, ranked habitations, allocation
TECHNOLOGIES USED
Languages, frameworks, hardware
Python 3.10 · NumPy 2.2 · FastAPI 0.141 · Uvicorn · scikit-learn 1.7 · pytest (227 tests). Front end is vanilla ES modules with Leaflet 1.9 vendored locally — no bundler, no build step. Ships as a Windows installer: PyInstaller 6.22 freezes the backend, Electron 33 provides the window. Hardware: commodity x86, 4 GB RAM, no GPU, no GDAL, runs fully offline.
Algorithms and national standards
Landslide: BIS IS 14496 (Part 2) LHEF rating scheme — the Geological Survey of India method. Trigger: Caine (1980) intensity-duration threshold. Terrain: Horn slope, Wang & Liu priority-flood, Garbrecht & Martz flat resolution, D8 routing, HAND (Nobre 2011), Beven-Kirkby wetness index. Flood: SCS Curve Number, Manning compound channel, FwDET depth. Erosion: Bruun (1962). Radar: Lee filter, Otsu threshold.
Data sources and machine learning
Live with no credentials: Open-Meteo (rainfall, soil moisture, CAPE) and the Copernicus Sentinel-1 catalogue. Connectors written for ISRO Bhoonidhi CartoDEM, Bhuvan, CWC gauges and GSI lithology. ML: random forests for radar water detection (F1 0.96 against a 0.66 physics baseline) and as a national red-zone surrogate (R² 0.77), both validated on held-out districts.

## Slide 4
FEASIBILITY AND VIABILITY
What is built, and what could break it
Every risk is stated with its mitigation. A pitch with no weaknesses has not been tested.
ALREADY BUILT AND TESTED
Working application: 22 districts, four terrain archetypes, four hazards.
227 automated tests, including the safety invariant that no relocation site may lie inside a Red Zone.
Median 1.5 s per district on a laptop. No GPU, no GDAL, no build step.
Live Copernicus Sentinel-1 catalogue query — real granules, no credentials.
Runs fully offline: relief basemap is rendered from our own elevation model.
RISKS
Lithology and structure need a Geological Survey of India map; two of six BIS LHEF factors are held neutral without it.
HAND assumes a level water surface and cannot see embankments finer than the DEM — the largest source of extent error.
Population is a Census 2011 projection, not a live count.
Erosion retreat over decades is sub-pixel at 160 m resolution.
Demo-mode input rasters are modelled, not observed.
MITIGATION
Geology raster loads through a documented interface and promotes the assessment to a complete LHEF rating.
Embankment barriers enter as a mask once digitised; the limitation is published rather than hidden.
WorldPop and real boundaries drop in without touching any model.
Retreat RATE is reported as the meaningful output; area is flagged as resolution-limited.
Permanent provenance badge on every screen and in every API response.

## Slide 5
IMPACT AND BENEFITS
Who it serves, and what changes
Primary user: State Disaster Management Authorities and District Magistrates planning proactive relocation.
946 km²
of Darbhanga modelled as Red Zone — 42% of the district
every 5 yr
the interval at which the worst habitations become unliveable
4
hazards assessed together: flood, landslide, waterlog, erosion
19%
of at-risk people placeable at assembled sites — the real gap
SOCIAL
Relocation becomes proactive and evidence-based instead of a response to the last disaster. Households are ranked by how many people are exposed and how often, so scarce resettlement funding reaches the villages that flood every fifth year rather than the loudest ones.
ECONOMIC
Ends the cycle of rebuilding the same assets in the same hazard zone. Identifies whether a district's binding constraint is land or site assembly — a distinction that changes whether the answer is acquisition, densification, or an inter-district decision.
GOVERNANCE
Every ranking publishes its weights and every hazard cites its standard, so a relocation order can be defended in an inquiry. The system states what it does not know — two BIS factors unmapped, population projected — rather than presenting an estimate as fact.
ROADMAP
NOW built and tested · P2 CartoDEM + GSI lithology · P3 CWC gauges, all 780 districts · P4 citizen hotline (IVR + LGD) as ground truth · P5 short code + Sachet CAP

## Slide 6
RESEARCH AND REFERENCES
Every step traces to a published method
Nothing here is invented. Standards first, and Indian standards where they exist.
STANDARDS AND LITERATURE
BIS IS 14496 (Part 2): 1998 — Landslide Hazard Zonation, LHEF scheme.
NDMA. National Disaster Management Plan; Guidelines on Floods.
Caine, N. (1980). Rainfall intensity-duration control of shallow landslides.
Bruun, P. (1962). Sea level rise as a cause of shore erosion.
Renno (2008); Nobre et al. (2011). Height Above Nearest Drainage.
Beven & Kirkby (1979). Variable contributing area model of basin hydrology.
Wang & Liu (2006). Efficient depression filling for flow routing.
Garbrecht & Martz (1997). Drainage direction over flat surfaces.
Cohen et al. (2018). FwDET floodwater depth estimation.
Otsu (1979); Lee (1980). Thresholding and speckle suppression.
Sphere Handbook. Shelter and settlement standards.
DATA SOURCES
Geological Survey of India
Lithology and structure for complete LHEF rating
ISRO Bhoonidhi / NRSC
bhoonidhi.nrsc.gov.in — CartoDEM, Resourcesat, EOS-04
Copernicus Data Space
dataspace.copernicus.eu — Sentinel-1 (connector live)
ISRO Bhuvan
bhuvan.nrsc.gov.in — NRSC hazard and flood layers
National Centre for Coastal Research
Shoreline change rates for the Indian coast
Census of India / WorldPop
Habitation population and settlement distribution
India Meteorological Department
Rainfall normals and extreme-value statistics
Survey of India / LGD
District and habitation boundaries